## Slide 1
PointNeXt 坐标量化敏感度分析
INT8 推理加速器 · 坐标精度该用几 bit ?
S3DIS · PointNeXt-S · 方案A (推理时 fake-quant, 不重训练)

## Slide 2
背景：坐标在 PointNeXt 里的用途
INT8 加速器只量化特征 (feature) 走 systolic array；坐标 (xyz) 单独成一条几何通路。
问题：几何通路的坐标，能不能也降到低位宽定点，省硬件？
坐标在网络中被用于 4 个地方：
  Encoder — 采样 (FPS/KD-tree)：决定保留哪些点
  Encoder — ball_query (bq)：决定每个点的 32 个邻居
  Encoder — dp 相对位置：p_j - p_center，作为 +3 通道喂 Conv
  Decoder — three_interpolation：3-NN 反距离插值上采样
坐标用途 | 用来做什么 | 输出
采样 sample | 选哪些点保留 (下采样) | 点的索引
ball_query (bq) | 算距离选邻居 | 邻居索引
dp 相对位置 | 算 p_j - p_center 当几何特征 | 数值 -> 喂 Conv
decoder 插值 | 3-NN 反距离加权上采样 | 插值特征

## Slide 3
第一步：全网络坐标量化 -> 掉 4 个点
把整个网络的坐标统一 fake-quant 到 n-bit，测试时直接评估 (不重训练)。
坐标精度 | test mIoU | 相对 FP32
FP32 | 61.73 | -
int8 | 57.73 | -4.00
int7 | 53.29 | -8.44
int6 | 34.12 | -27.61
int5 | 14.79 | -46.94
int4 | 6.57 | -55.16
结论
int8 就掉 4 个点，断崖在 int7->int6。
但这是「全网络」量化 — 分不清是哪个
环节引起的。
-> 需要逐环节隔离。

## Slide 4
第二步：Decoder 隔离 -> 插值用 int8 几乎免费
只量化 decoder three_interpolation 的坐标，encoder 全程保持 FP32。
实验 | 配置 | mIoU | 相对 FP32
fp32 基准 | decoder 全 FP32 | 61.73 | -
decoder int8 | 选邻居+权重都 int8 | 61.66 | -0.07
A: 只 id int8 | 选邻居 int8 / 权重 FP32 | 61.69 | -0.04
B: 只权重 int8 | 选邻居 FP32 / 权重 int8 | 61.73 | 0.00
int12/int16/FP16 | 更高精度 | 61.73 | 0.00
结论：decoder 插值对坐标精度极不敏感 — int8 只掉 0.07 mIoU，基本免费。
  插值权重是反距离的平滑函数，坐标小误差 -> 权重小误差 -> 加权平均几乎不变。
-> 那 4 个点的掉点不在 decoder。真凶在 encoder。

## Slide 5
第三步：Encoder 三路隔离 -> 超加性效应
实验 | sample | bq | dp | mIoU | 掉点
enc_fp32 | FP32 | FP32 | FP32 | 61.73 | -
enc_all8 | int8 | int8 | int8 | 57.78 | -3.95
enc_sample8 | int8 | FP32 | FP32 | 61.74 | +0.01
enc_bq8 | FP32 | int8 | FP32 | 61.01 | -0.72
enc_dp8 | FP32 | FP32 | int8 | 60.64 | -1.09
超加性 (super-additive)
  sample 单独 : -0.01
  bq 单独 : -0.72
  dp 单独 : -1.09
  三者之和 : 约 -1.8
  但 all8 实测 : -3.95
关键发现
1) 采样坐标 int8 完全免费 (+0.01) — FPS/KD-tree 单元可放心用 int8。
2) bq 和 dp 单独量化各掉 ~1 点；同时量化掉 ~4 点。
  交互项 = 3.95 - 1.8 = 2.1，比任何单项都大。
3) bq 选错邻居 + dp 算错位置 -> 几何特征双重失真，跨 4 个 stage 累积放大。
-> 不能只修一个：bq 和 dp 必须一起保高精度。

## Slide 6
第四步：完整 4x4 网格 -> 只要任一路 >=9bit 即恢复
采样固定 int8，完整覆盖 bq x dp 的 8/9/10/12 共 16 种组合，规律铁证。
bq＼dp | 8 | 9 | 10 | 12
8 | 57.78 | 60.96 | 61.10 | 60.97
9 | 60.52 | 61.76 | 61.86 | 61.73
10 | 60.52 | 61.77 | 61.87 | 61.74
12 | 60.58 | 61.79 | 61.88 | 61.76
test mIoU, FP32 基准 = 61.73
🟥 两路都 int8 = 灾难 🟨 任一路 int8 = 单路惩罚
🟩 两路都 >=9bit = 完全恢复
关键发现 (16 格全跑完)
🔴 唯一灾难点 (8,8) = 57.78
🟡 dp=8 整列 60.52-60.58 (单路 -1.2)
🟡 bq=8 整行 60.96-61.10 (单路 -0.7)
🟢 内 3x3 共 9 格 = 61.73-61.88
  噪声仅 ~0.15，完全恢复
整个悬崖只在 8->9 一个 bit。
任一路 >=9bit，-2 的交互项立刻消失。

## Slide 7
补充实验：dp post-normalize 量化扫描 -> 5-bit 就够
控制变量：源坐标全 FP32，只把 /radius 之后的 dp_norm ∈ [-1,+1] 量化到 N bit。
直接验证硬件 (S=1/2^(N-1), Z=2^(N-1)) 那一步是否引入精度损失。
nbits | levels in [-1,+1] | mIoU | vs FP32 (61.73)
8 | 256 | 61.74 | +0.01
6 | 64 | 61.81 | +0.08
5 | 32 | 61.73 | 0.00
4 | 16 | 61.45 | -0.28
3 | 8 | 60.33 | -1.40
2 | 4 | 55.13 | -6.60
决定性结论
post=8 (uint8) ≈ 基准 -> /radius + post-quant 完全免费。
post=5 (32 级) 仍完全无损 -> 硬件其实可以更激进。
门槛在 4->3 bit (16->8 级)，post=2 才灾难。
→ 假说 A 锁定：之前 (8,8) 的 -3.95 灾难
  完全是源坐标 4cm 步长 / voxel 碰撞造成。
→ 硬件用 uint8 (1/128, 128) 是过度安全；
  甚至 uint5 也免费，可省 3 bit 通道带宽。

## Slide 8
结论：给硬件的坐标精度方案 (完整版)
坐标用途 | int8 掉点 | 最小可用精度
Decoder 插值 (源坐标) | -0.07 | int8 免费
Encoder 采样 (源坐标) | -0.01 | int8 免费
Encoder ball_query (源坐标) | -0.72 (单独) | >= 9-bit
Encoder dp 源坐标精度 | -1.09 (单独) | >= 9-bit
Encoder bq + dp 同时 (源) | -3.95 | 两路都 >= 9-bit
dp post-normalize quant | 0.00 | uint5 已够, uint8 过度安全
最终硬件建议
源坐标统一用 9-10 bit 定点 (int8 触发碰撞灾难，int9 完全恢复，int10 留余量)。
dp post-normalize quant 用 uint8 (S=1/128, Z=128) 即可；想省带宽可降到 uint5。
两个量化点解耦：源坐标精度决定 dp 真值准不准，post-normalize quant 只决定网格疏密。
不需要 FP16、不需要 topK refine、不需要混合精度 — 简单定点几何单元覆盖全网络。
方案A (不重训练) 结论 -> 9-bit 定点是 drop-in 的，连 QAT 都省了。

## Slide 9
Training-Free Validation: block FPS drops in with no accuracy loss
Ablation ladder (global-FPS checkpoint, mode=test, no finetune)
step | config | mIoU | Δ vs A0
A0 | global FPS (baseline) | 62.98 | —
A1 | block FPS (leaf 1500) | 63.03 | +0.05
A2 | + int8 sample coords | 62.98 | 0.00
A3 | + bq/dp int8 (naive) | 60.16 | −2.82
A3s | + bq/dp 9-bit (ours) | 62.92 | −0.06
[Z] block FPS retrain-free cost = +0.05 → zero loss (slightly up)
[A] full KDPoint config (block FPS + 9-bit coords) = −0.06 → near-lossless
A3 naive all-int8 = −2.82 → why the 9-bit sidecar is needed (counter-example)
Leaf-size sweep (block FPS, retrain-free)
leaf | 256 | 512 | 1024 | 1500 | 3000 | 24000
mIoU | 62.72 | 62.88 | 62.97 | 63.03 | 63.07 | 63.05
Flat across 256 → 24000 (62.72–63.07, span 0.35).
No leaf triggers any drop → retrain-free property is
  independent of leaf tuning; hardware picks any size.
All ≥ baseline 62.98 except leaf=256 (−0.26, still noise).
Takeaway
Three-way exactness now complete: exact KD partition + exact BQ/KNN
  + retrain-free block FPS ([Z]=+0.05). KDPoint needs NO retraining,
  differentiating from FractalCloud's retrain-based pipeline.
S3DIS Area-5 · PointNeXt-S · 100-epoch global-FPS checkpoint (val 61.93) · test = sliding-window + voting (≈ +1 over val). Coordinate-quant only; weight/activation INT8 PTQ stacks on top.

## Slide 10
Block FPS retrain-free generalizes: 2 models x 3 datasets
[Z] block FPS retrain-free cost (A0 global -> A1 block)
model x dataset | A0 | A1 | [Z]
PointNeXt x S3DIS | 62.98 | 63.03 | +0.05
PointNeXt x ModelNet40 | 92.10 | 91.90 | -0.20
PointNeXt x ShapeNet | 86.28 | 85.98 | -0.30
PointNet++ x S3DIS | 60.42 | 60.33 | -0.09
PointNet++ x ModelNet40 | 91.09 | 90.60 | -0.49
PointNet++ x ShapeNet | 86.28 | 85.60 | -0.68
[A] full config (block FPS + 9-bit coords) + naive counter
model x dataset | A3-safe | naive int8
PointNeXt x S3DIS | -0.06 | 60.16
PointNeXt x ModelNet40 | -0.37 | 91.82
PointNeXt x ShapeNet | -0.30 (leaf1024) | 78.76
PointNet++ x S3DIS | -0.10 | 58.44
PointNet++ x ModelNet40 | -0.33 | 90.80
PointNet++ x ShapeNet | -0.69 | 85.55
Takeaway
5/6 cells near-lossless retrain-free: -0.05 ~ -0.68 mIoU/OA.
* PointNeXt x ShapeNet: default leaf=128 hurts (-7.53); larger leaf recovers
  (leaf=512 -> -1.34, leaf=2048=global -> 0). Leaf must scale to task; see next slide.
Naive all-int8 coords always collapses (e.g. S3DIS -2~-3); 9-bit sidecar restores it.
S3DIS/ModelNet40/ShapeNet * PointNeXt-S / PointNet++ * test (seg/partseg=voting, cls=OA) * inference-time, no retraining.

## Slide 11
INT8 PTQ near-lossless + ShapeNet leaf-size sensitivity
INT8 PTQ (weights+acts), stacked on block FPS
model x dataset | FP32 | INT8 | delta
PointNeXt x S3DIS | 61.43 | 61.41 | -0.02
PointNeXt x ModelNet40 | 91.90 | 91.69 | -0.20
PointNeXt x ShapeNet | 76.35 | 76.06 | -0.30
PointNet++ x S3DIS | 58.96 | 57.51 | -1.45
PointNet++ x ModelNet40 | 90.60 | 90.56 | -0.04
PointNet++ x ShapeNet | 84.17 | 83.32 | -0.85
All 6 cells < 2% INT8 cost; PointNeXt all <=-0.30.
PN++ x S3DIS -1.45 (largest; RGB feats + ConvPool
  more quant-sensitive; calib 30->50 didn't change).
ShapeNet leaf sweep (block FPS, retrain-free)
leaf | 32 | 64 | 128 | 256 | 512 | 2048
PointNeXt | 76.7 | 77.3 | 78.8 | 81.5 | 84.9 | 86.3
PointNet++ | 85.1 | 85.4 | 85.6 | 85.8 | 86.1 | 86.3
PointNeXt x ShapeNet: monotonic in leaf -- small leaf
  breaks fine part boundaries; leaf=2048(=global) full recovery.
PointNet++: flat (stride-4 aggressive downsample is
  robust to block locality). Same dataset, opposite sensitivity.
Lesson: leaf scales with task -- small-cloud part-seg on
  high-capacity PointNeXt needs large leaf; everything else is free.
PTQ FP32 != ladder A0: PTQ uses single-pass validate on the block-FPS model; ladder uses test+voting on global FPS. delta is the quant cost.